Create wheels using rigid body constraints – hinge – set x-axis to be along axle of wheel
cylinder collision box seems to work well for wheels
turn on local collision if the wheels are very close to the vehicle to prevent the two from colliding

damping – resistance to motion – simulates air drag, rolling resistance, etc...
Damp is the damping factor for the linear velocity, and Rot Damp is the damping factor for the angular velocity. The factor expresses the decrease in velocity over one second. Currently, the damping is regardless of the mass of the objects, so light objects drop as fast as heavy objects.

## What's the difference between damping and friction?
Damping is a decrease of velocity in % per second. Damping is useful to achieve a maximum speed. The larger the speed the greater the absolute decrease of speed due to drag. The maximum speed is attained when the acceleration due to forces equals the deceleration due to drag. Damping is also useful for damping out unwanted oscillations due to springs.
Friction is a force tangent to the contact surface. The friction force has a maximum that is linear to the normal, i.e., the force that presses the objects against each other, (the weight of the object).  TheFriction value denotes the Coulomb friction coeffcient, i.e. the ratio of the maximum friction force and the normal force.  A larger Friction value will allow for a larger maximum friction. For a sliding object the friction force will always be the maximum friction force. For a stationary object the friction force will cancel out any tangent force that is less than the maximum friction. If the tangent force is larger than the maximum friction than the object will start sliding.

## What is Anisotropic Friction?
For some objects you need to have different friction in different directions. For instance a skate board will experience relatively little friction when moving it  forward and backward, but a lot of friction when moving it side to side. This is called anisotropic friction. Anisotropic friction is enabled by selecting the Anisotropic button in the Real-time window.  After selecting this button, three sliders will appear in which the relative coefficient for each of the local axes can be set. A relative coefficient of zero denotes that along the corresponding axis no friction is experienced. A relative coefficient of one denotes that the full friction applies along the corresponding axis.

max tire friction on a dry road ~0.7
wet road ~0.4
http://hyperphysics.phy-astr.gsu.edu/hbase/mechanics/frictire.html

rolling friction:
A rolling wheel requires a certain amount of friction so that the point of contact of the wheel with the surface will not slip. The amount of traction which can be obtained for an auto tire is determined by the coefficient of static friction between the tire and the road. If the wheel is locked and sliding, the force of friction is determined by the coefficient of kinetic friction and is usually significantly less.
Assuming that a wheel is rolling without slipping, the surface friction does no work against the motion of the wheel and no energy is lost at that point. However, there is some loss of energy and some deceleration from friction for any real wheel, and this is sometimes referred to as rolling friction. It is partly friction at the axle and can be partly due to flexing of the wheel which will dissipate some energy. Figures of 0.02 to 0.06 have been reported as effective coefficients of rolling friction for automobile tires, compared to about 0.8 for the maximum static friction coefficient between the tire and the road.
http://hyperphysics.phy-astr.gsu.edu/hbase/frict2.html

#### Approximate coefficients of friction
Materials		Static friction,
		Dry & clean	Lubricated
Aluminum	Steel	0.61
Copper	Steel	0.53
Brass	Steel	0.51
Cast iron	Copper	1.05
Cast iron	Zinc	0.85
Concrete (wet)	Rubber	0.30
Concrete (dry)	Rubber	1.0
Concrete	Wood	0.62[9]
Copper	Glass	0.68
Glass	Glass	0.94
Metal	Wood	0.2–0.6[9]	0.2 (wet)[9]
Polythene	Steel	0.2[10]	0.2[10]
Steel	Steel	0.80[10]	0.16[10]
Steel	Teflon	0.04[10]	0.04[10]
Teflon	Teflon	0.04[10]	0.04[10]
Wood	Wood	0.25–0.5[9]	0.2 (wet)[9]

From wikipedia

form factor:
  1. all the mass is in the center
     0.4 the body is solid (with homogeneous density)
     1.0 all the mass is in the surface (hollow body)
    http://blenderartists.org/forum/archive/index.php/t-138645.html

vehicle modeling with constraints
http://bulletphysics.org/Bullet/phpBB3/viewtopic.php?f=9&t=7074

maddock document on ray cast vehicle simulation
https://docs.google.com/document/edit?id=18edpOwtGgCwNyvakS78jxMajCuezotCU_0iezcwiFQc

## Calculating the Slip Angle
Pacejka uses the slip angle to calculate the maximum friction force.
              const btRigidBody* const chassis = vehicle->getRigidBody();
              const btWheelInfo& wheel_info = vehicle->getWheelInfo(i);
              // Calculate velocity of wheel wrt ground
              btVector3 rel_pos1 = wheel_info.m_raycastInfo.m_contactPointWS - chassis->getCenterOfMassPosition();
              btVector3 vel = chassis->getVelocityInLocalPoint(rel_pos1);

              // Calculate velocity in x & y
              btScalar vz = -vehicle->getForward(i).dot(vel);
              btScalar vx = vehicle->getAxle(i).dot(vel);

              // Calculate slip angle of wheel.
              btScalar slip_angle = btAtan2(vx, btFabs(vz));

accuracy of USARSim
http://www.mit.edu/~robbel/PerMIS07.Final_Pepper.pdf

models:

http://www.edgedsign.com/Peoples_Street_MOUT_database.html

wheel object members:
['__class__', '__contains__', '__delattr__', '__delitem__', '__doc__', '__eq__', '__format__', '__ge__', '__getattribute__', '__getitem__', '__gt__', '__hash__', '__init__', '__le__', '__lt__', '__ne__', '__new__', '__reduce__', '__reduce_ex__', '__repr__', '__setattr__', '__setitem__', '__sizeof__', '__str__', '__subclasshook__', 'actuators', 'alignAxisToVect', 'angularVelocity', 'applyForce', 'applyImpulse', 'applyMovement', 'applyRotation', 'applyTorque', 'attrDict', 'children', 'childrenRecursive', 'color', 'controllers', 'disableRigidBody', 'enableRigidBody', 'endObject', 'get', 'getAngularVelocity', 'getAxisVect', 'getDistanceTo', 'getLinearVelocity', 'getPhysicsId', 'getPropertyNames', 'getReactionForce', 'getVectTo', 'getVelocity', 'invalid', 'life', 'linVelocityMax', 'linVelocityMin', 'linearVelocity', 'localAngularVelocity', 'localInertia', 'localLinearVelocity', 'localOrientation', 'localPosition', 'localScale', 'mass', 'meshes', 'name', 'occlusion', 'orientation', 'parent', 'position', 'rayCast', 'rayCastTo', 'reinstancePhysicsMesh', 'removeParent', 'replaceMesh', 'restoreDynamics', 'scaling', 'sendMessage', 'sensors', 'setAngularVelocity', 'setCollisionMargin', 'setLinearVelocity', 'setOcclusion', 'setParent', 'setVisible', 'state', 'suspendDynamics', 'timeOffset', 'visible', 'worldAngularVelocity', 'worldLinearVelocity', 'worldOrientation', 'worldPosition', 'worldScale']

scene object members:
######## ROBOT 'rmp400_chassis' INITIALIZING ########
['__class__', '__contains__', '__delattr__', '__delitem__', '__doc__', '__eq__', '__format__', '__ge__', '__getattribute__', '__getitem__', '__gt__', '__hash__', '__init__', '__le__', '__lt__', '__ne__', '__new__', '__reduce__', '__reduce_ex__', '__repr__', '__setattr__', '__setitem__', '__sizeof__', '__str__', '__subclasshook__', 'active_camera', 'activity_culling', 'activity_culling_radius', 'addObject', 'cameras', 'dbvt_culling', 'end', 'get', 'invalid', 'lights', 'name', 'objects', 'objectsInactive', 'post_draw', 'pre_draw', 'replace', 'restart', 'resume', 'suspend', 'suspended']

scene.objects members:
['__add__', '__class__', '__contains__', '__delattr__', '__doc__', '__eq__', '__format__', '__ge__', '__getattribute__', '__getitem__', '__gt__', '__hash__', '__init__', '__le__', '__len__', '__lt__', '__ne__', '__new__', '__reduce__', '__reduce_ex__', '__repr__', '__setattr__', '__sizeof__', '__str__', '__subclasshook__', 'append', 'count', 'from_id', 'get', 'index', 'invalid', 'name', 'reverse']